## Slide 1: Frequency Response and Control in Power Systems
Megan Swanson
SUPERB Project
July 2017

## Slide 2: Overview
Purpose and Motivation
Background
Modeling
Swing Equation
Control Models:
  Constant Power
  Droop Control
  Virtual Inertia
Proposed methods

## Slide 3: Purpose and Motivation
The purpose of this project is to analyze the effect of increased renewable power source penetration on the frequency response of the grid.
With more and more renewable sources being used, we need to know how these changes will effect the gird in terms of safety and robustness.
Notes: The purpose of this project is to model a power system and analyze the frequency response of the system after disturbances with respect to different levels of inertia in the system

## Slide 4: Background
Inertia
  Lower inertia = faster frequency response
Damping
  Lower damping = faster frequency response
Faster frequency response = more severe consequences
Renewables:
No inertia (H = 0)
Increased frequency response
Less control
Notes: Frequency Response is how the system responds after a significant loss of generation.
Frequency control in power systems is made possible because of the rotational inertia from conventional generators in the system. This inertia is what keeps the system frequency from deviating too much when generation losses occur because the inertia from the generators keep spinning at the same rate for a set time and the PFR is able to kick in before it changes too much. Without this inertia, or with decreased inertia, the system frequency will change much faster, often too quickly for the PFR to to kick in before it drops below the safe values which can cause a cascade of trips and interrupt service.

## Slide 5: Modeling
Simulation software
  Complicated (many variables)
  Expensive (time and money)
Full network models
  Complicated (many variables)
  Time
Simplified Models (Aggregated Swing eq. Average Freq.)
  Marginally less accurate
  Easy to use
Notes: In power systems, the frequency response can be modeled with equations or simulation software. Simulations offer very precise results, however, they require knowledge of many different parameters related to all components of a system and are therefore difficult to use for large systems. Similarly, full network models have a similar restraint in which many parameters are necessary to be concise and they become very difficult to manage for large systems. Therefore, researchers tend to use simplified models to examine larger systems because they can be adapted to take less variables and still produce a relatively accurate result.

## Slide 6: Swing Equation
Aggregate Swing Equation:
Assuming:
[1]
Notes: We are going to use the swing equation to model the frequency response because it is more accurate than…
We are using the aggregated swing equation to adapt the equation to model a whole network.

## Slide 7: Results

## Slide 8: Constant Power
Swing Equation:
[2]

## Slide 9: Results

## Slide 10: Droop Control
Control Variable:
Swing Equation:
or
[2]

## Slide 11: Results

## Slide 12: Virtual Inertia
Control Variable:
Swing Equation:
or
[2]

## Slide 13: Results

## Slide 15: Proposed Methods
Synthetic or Virtual Inertia
  Pros: Increases overall inertia
  Cons: High cost to update all facilities with the necessary control mechanisms
Energy Storage Systems
  Pros: Provides reserve power
  Cons: Costly
Deloading
  Pros: Provides primary control for longer periods of time
  Cons: Inefficient and expensive

## Slide 16: References
[1]A. Ulbig,, T. Borsche, and G. Andersson, "Impact of Low Rotational Inertia on Power System Stability and Operation", IFAC Proceedings Volumes, vol. 47, no. 3, pp. 7290-7297, 2014.
[2]A. Ulbig, T. Rinke, S. Chatzivasileiadis and G. Andersson, "Predictive control for real-time frequency regulation and rotational inertia provision in power systems", 52nd IEEE Conference on Decision and Control, pp. 2946-2953, 2013.
[3]B. Poolla, S. Bolognani and F. Dorfler, "Optimal Placement of Virtual Inertia in Power Grids", IEEE Transactions on Automatic Control, vol., no. 99, pp. 1-1, 2016.
[4]E. Mallada, "iDroop: A Dynamic Droop controller to decouple power grid's steady-state and dynamic performance", 2016 IEEE 55th Conference on Decision and Control (CDC), 2016.
[5]H. Chiang, F. Wu and P. Varaiya, "Foundations of direct methods for power system transient stability analysis", IEEE Transactions on Circuits and Systems, vol. 34, no. 2, pp. 160-173, 1987.
[6]M. Chan, R. Dunlop and F. Schweppe, "Dynamic Equivalents for Average System Frequency Behavior Following Major Disturbances", IEEE Transactions on Power Apparatus and Systems, vol. -91, no. 4, pp. 1637-1642, 1972.
[7]N. Miller, M. Shao, S. Venkataraman, C. Loutan and M. Rothleder, "Frequency response of California and WECC under high wind and solar conditions", 2012 IEEE Power and Energy Society General Meeting, pp. 1-8, 2012.
[8]P. Varaiya, F. Wu and R. Chen, "Direct methods for transient stability analysis of power systems: Recent results", Proceedings of the IEEE, vol. 73, no. 12, pp. 1703-1715, 1985.
[9]R. Yan and T. Saha, "Frequency response estimation method for high wind penetration considering wind turbine frequency support functions", IET Renewable Power Generation, vol. 9, no. 7, pp. 775-782, 2015.