## Slide 1: Frequency Response and Control in Power Systems
Megan Swanson
SUPERB Project
July 2017

## Slide 2: Overview
Purpose
Background
Modeling
Swing Equation
Results
Impact of Renewables
Proposed methods
Results

## Slide 3: Purpose
The purpose of this review is to increase my understanding of frequency response and control in power systems with a focus on how variable renewable energy affects the system.

## Slide 4: Frequency Response and Control in Power Systems
Inertia
  Lower inertia = faster frequency response
Damping
  Lower damping = faster frequency response
Faster frequency response = more severe consequences
Notes: Frequency Response is how the system responds after a significant loss of generation.
Frequency control in power systems is made possible because of the rotational inertia from conventional generators in the system. This inertia is what keeps the system frequency from deviating too much when generation losses occur because the inertia from the generators keep spinning at the same rate for a set time and the PFR is able to kick in before it changes too much. Without this inertia, or with decreased inertia, the system frequency will change much faster, often too quickly for the PFR to to kick in before it drops below the safe values which can cause a cascade of trips and interrupt service.

## Slide 5: Modeling
Simulation software (i.e. “insert simulation software name here”)
  Used as a comparison tool to validate simplified models in THIS paper
  Complicated (many variables)
  Expensive (time and money)
Notes: In power systems, the frequency response can be modeled with equations or simulation software. Simulations offer very precise results, however, they require knowledge of many different parameters related to all components of a system and are therefore difficult to use for large systems. Similarly, full network models have a similar restraint in which many parameters are necessary to be concise and they become very difficult to manage for large systems. Therefore, researchers tend to use simplified models to examine larger systems because they can be adapted to take less variables and still produce a relatively accurate result.

## Slide 6: Modeling
Full network models (as in THIS paper)
  Complicated (many variables)
  Time
Notes: Full network modeling requires information about all components in the network for each parameter used which is unfeasible for larger systems. Because of the great number of inputs, it also takes a lot of time.

## Slide 7: Modeling
Simplified Models (Aggregated Swing eq. Average Freq.)
  Marginally less accurate
  Easy to use
Notes: Simplified models are less accurate but require much less information which makes it feasible for large network modeling. Also, as THIS paper has shown, the Aggregated Swing eq. is pretty accurate when compared to a simulation.

## Slide 8: Swing Equation (no control)
Aggregate Swing Equation:
Assuming:
  Varying ( ) as a function of time (shown on next slide)
[1]
Notes: We are going to use the swing equation to model the frequency response because it is more accurate than…
We are using the aggregated swing equation to adapt the equation to model a whole network.

## Slide 9: Results

## Slide 10: Impact of Renewables
No inertia (H = 0)
Increased frequency response
Less control
Notes: Variable renewable energy sources like wind and solar do not contribute any rotational inertia. Because of this, when more renewables are incorporated into power systems, the overall system inertia decreases. A decrease in inertia means that the frequency response in the event of a major fault or loss of generation (basically any major power imbalance) will be much more severe because the entire system will react faster when there is less inertia to maintain the frequency. This response will be too quick for the primary frequency response controls and could cause cascading trips and wide spread blackouts.

## Slide 12: Proposed Methods
Synthetic or Virtual Inertia
Energy Storage Systems
Deloading

## Slide 13: Virtual Inertia
Pros: Increases overall inertia
Cons: High cost to update all facilities with the necessary control mechanisms

## Slide 14: Energy Storage Systems
Pros: Provides reserve power
Cons: Costly

## Slide 15: Deloading
Pros: Provides primary control for longer periods of time
Cons: Inefficient and expensive

## Slide 16: References
[1] A. Ulbig, T. Borsche and G. Andersson, "Impact of Low Rotational Inertia on Power System Stability and Operation", IFAC Proceedings Volumes, vol. 47, no. 3, pp. 7290-7297, 2014.
[2] H. Chiang, F. Wu and P. Varaiya, "Foundations of direct methods for power system transient stability analysis", IEEE Transactions on Circuits and Systems, vol. 34, no. 2, pp. 160-173, 1987.
[3] P. Varaiya, F. Wu and R. Chen, "Direct methods for transient stability analysis of power systems: Recent results", Proceedings of the IEEE, vol. 73, no. 12, pp. 1703-1715, 1985.
[4 ]R. Yan and T. Saha, "Frequency response estimation method for high wind penetration considering wind turbine frequency support functions", IET Renewable Power Generation, vol. 9, no. 7, pp. 775-782, 2015.
[5] M. Chan, R. Dunlop and F. Schweppe, "Dynamic Equivalents for Average System Frequency Behavior Following Major Disturbances", IEEE Transactions on Power Apparatus and Systems, vol. - 91, no. 4, pp. 1637-1642, 1972.
[6] B. Poolla, S. Bolognani and F. Dorfler, "Optimal Placement of Virtual Inertia in Power Grids", IEEE Transactions on Automatic Control, vol., no. 99, pp. 1-1, 2016.
[7] N. Miller, M. Shao, S. Venkataraman, C. Loutan and M. Rothleder, "Frequency response of California and WECC under high wind and solar conditions", 2012 IEEE Power and Energy Society General Meeting, pp. 1-8, 2012.